## Slide 1: New Orleans Demand Response Potential Study: DRAFT RESULTS
American Council for an Energy-Efficient Economy
(ACEEE)
July 2018

## Slide 2: Methodology
Literature review
Determine taxonomy of programs to examine
Create database of demand response programs & data
  In region
  Out of region
Collect data from Entergy New Orleans
Estimate program savings per participant, participation rates,& costs based on program research
Input data to demand response models

## Slide 3: DR Programs
Residential incentive-based DR
  Direct load control (DLC) program
  Automated DR -bring your own device (BYOD) program, which incentivizes wifi-enabled thermostats that trigger AC cycling
Residential time-based pricing DR, including
  peak time rebates (PTR) with and w/o enabling technologies
  critical peak pricing (CPP) with and w/o enabling technologies
Commercial and industrial (C&I)
  Standard offer program
  Direct load control

## Slide 4: Data Sources
Entergy New Orleans data
Utility demand response program filings from in-region
  Entergy Louisiana
  Entergy Arkansas
  Arizona Public Service
  Oklahoma Gas & Electric
  AEP Texas Central and other TX programs
  Etc.
Federal Energy Regulatory Commission (FERC) national
demand response potential study
Arcturus study on dynamic pricing

## Slide 5: Draft Results: Scenario 1 “Base case” and Peak-Time Rebates (PTR)
Program | Metric | 2018 | 2027 | 2037
Residential direct load control (DLC) and bring your own device (BYOD) | Peak demand savings (MWs) | 1.97 | 13.6 | 16.8
 | Cost | $207,249 | $940,836 | $1,126,367
NPV B/C ratio | 1.37 |  |  | 
Residential peak time rebate w/ and w/o tech. | Peak demand savings (MWs) | 5.17 | 9.54 | 10.6
 | Cost | $171,212 | $315,827 | $351,929
NPV B/C ratio | 1.89 |  |  | 
Commercial & industrial Standard Offer Program (SOP) | Peak demand savings (MWs) | 0.35 | 3.63 | 7.50
 | Cost | $13,103 | $135,296 | $279,416
NPV B/C ratio | 2.67 |  |  | 

## Slide 6: Draft Results: Scenario 2 “High case” and Critical Peak Pricing (CPP)
Program | Metric | 2018 | 2027 | 2037
Residential direct load control (DLC) and bring your own device (BYOD) | Peak demand savings (MWs) | 3.94 | 27.3 | 33.6
 | Cost | $414,499 | $1,881,673 | $2,252,735
NPV B/C ratio | 1.37 |  |  | 
Residential critical peak pricing w/ and w/o tech. | Peak demand savings (MWs) | 5.83 | 10.8 | 12.0
 | Cost | *draft results not yet available |  | 
NPV B/C ratio |  | *draft results not yet available |  | 
Commercial & industrial Standard Offer Program (SOP) | Peak demand savings (MWs) | 2.46 | 6.79 | 11.9
 | Cost | $83,780 | $241,111 | $426,359
NPV B/C ratio | 2.75 |  |  |